| Date of Inspection: Name of Inspecting Officer: Appointment Date & Time of Site Visit: Weather Condition: Project Title: Location of Site : Project Duration: Type of Present Construction Activity: PUB Permit Number: Owner / Developer: QP for Project: QECP for ECM: ECO: Owner / Developer's Representative on-site: Date of ECM Plan: Last Date of ECM Plan Review: ADDITIONAL INFORMATION Date & Time of Previous Site Visit: Date Of Last Inspection Report: Issues Identified In Previous Site Visit: This site inspection has been certified by: QP / QECP: Signature: Date: Contractor: Signature: Date: Owner/Developer: Signature: Date: Note: Earth Control Measures is for the treatment of silty water due to rain water. Construction wastewater (slurry, bentonite..etc) due to tunnelling, boring..etc shall be separately treated. | S/N BEST MANAGEMENT PRACTICES INSPECTION COMPLIANCE ACTIONS 1 Construction Sequence & Scheduling Clearing of construction areas carried out in phases? Yes / No / NA 2 Stockpiles of Earth Materials Stockpile location according to ECM plan? Yes / No / NA 3 Stablization through laying of milled waste, lean concrete, turfing …etc Location according to ECM schedule? Yes / No / NA Construction according to ECM details? Yes / No / NA Any signs of damage at lean concrete areas? Yes / No / NA Any signs of damage at milled waste areas? Yes / No / NA Any signs of damage at turfed areas? Yes / No / NA 4 Stockpiles of Earth Materials Stockpile location according to ECM plan? Yes / No / NA Protected against erosion? Yes / No / NA Protected against sedimentation? Yes / No / NA 5 Silt Traps Installation of silt traps including location according to ECM schedule? Yes / No / NA Installation of silt traps according to ECM plan including no.s & size? Yes / No / NA Silt Traps damaged? Yes / No / NA 6 Sedimentation Basins / Storage Ponds Installation of basins / ponds including location according to ECM schedule? Yes / No / NA Installation of basins / ponds according to ECM plan including no.s? Yes / No / NA Concentration of TSS in effluent (outlet of discharge) < 50mg/l? Yes / No / NA Sediment filled to within 300mm of water discharge level of outflow structure? Yes / No / NA Sedimentation basins inlet / outlet choked? Yes / No / NA Protected against sedimentation? Yes / No / NA 7 Treatment Units / Polymer Blocks Treatment unit(s) in operation? Yes / No / NA Polymer blocks used / adequate? Yes / No / NA 8 Perimeter cut-off drains Installation of cut-off drains including location according to ECM schedule? Yes / No / NA Installation of cut-off drains according to ECM plan including lengths? Yes / No / NA Cut-off drain lined? Yes / No / NA Any signs of inadequate capacity? (flooding) Yes / No / NA Any obstruction / sediment? Yes / No / NA Any signs of damage? Yes / No / NA 9 Wheeled wash areas, entry/exit points Location according to ECM plan? Yes / No / NA Construction according to details? Yes / No / NA Any signs of damage? Yes / No / NA Run-off (from wheeled wash areas) and overflow / discharge channeled to suitable areas for proper treatment? Yes / No / NA Any signs of silty water from these areas into public drains (drains / roads / etc)? Yes / No / NA 10 Others Any areas without/inedequate ECM? Yes / No / NA Public drains at discharge points silted? Yes / No / NA Public drains in vicinity of site silted / obstructed? Yes / No / NA Run-off from site not channeled through silt fences / cut-off drains / silt traps? Yes / No / NA Any discharge of water into public drains? Yes / No / NA Earth surfaces / slops adjacent to any drain not turfed, paved or covered? Yes / No / NA Any other observations / comments: |
| --- | --- |